VLSI Lab Assignment – 4

Aim And Objective : To understand the working of digital VLSI four bit wallace multiplier using the Xilinx and Cadence tools.

Introduction : Four bit wallace multiplier consists of two 4 - bit input vectors ‘a’ and ‘b’. The multiplier works on the basic optimisation model in which the task of multiplying is divided into differrent stages and in each stage all the operations are happening independently. Outputs in each stage are calculated based on the previous stage output only or only based on the inputs directly available.

Procedure : In this assignment , we begin with writing basic verilog codes for the half – adder ,full – adder and then 4-bit wallace tree multiplier in which we call the half – adder and full – adder functions. Then we generate the RTL schematics from Xilinx . We then write the code for the corresponding test benches to simulate the codes written and generate the timing diagrams . I have included the RTL schematics and Timing diagrams from Xilinx in my folders . Then we also run our code on Spartan 3E boards hence we create a constraints file and implement our design to see the area ,power and timing reports.
 Then we open cadence and generate snapshots in order to simulate timing waveforms . I have also included the corresponding timing diagrams screenshots in my folders .
We then edit the rc_script file in order to run genus for that specific code . After that we run genus . In genus we take screenshots of the RTL schematic that is generated . Running genus also generates various files such as the area , power , timing report and netlists . We then save these files and I have included all these files in my folders .
We then run innovus . From innovus we get the layout diagram . We also get the file we send to the fabrication station (enc). We also generate the area , power and timing diagrams which I have included in my folders.

Results And Discussion : The 4 – bit wallace tree multiplier shows that time delay to compute the product is less for this compared to normal 4 - bit multiplier but the area and power is more. All the computations in the given stage are calculated independently and the area is optimised as we use half and full adders are used in the places required instead of the normal 4 bit full adders.

Conclusion : The impletation makes us realise that dividing the problems into some stages that are each computed independently reduces the time delay of the sult from the inputs when compared with a normal 4-bit multiplier.

References : 1 . www.asic-world.com
        2. Videos uploaded by Mayank and Kunal sir on	moodle.

Rahul Kashyap
(2018102037)